## Slide 1: EE-299: Design of a Single Phase Inverter
Project Presentation
M. Raghav Gopal
Supervisor: Prof. Ragavan K.

## Slide 2: Inverter – DC to AC converter
Use Cases:
Grid – tie inverter.
VFD for electrical machines.
Classification:
VSI vs CSI
Pure Sine Wave vs Modified Sine wave
Notes: Grid tie inverters converts DC to AC suitable to inject into the grid at the same voltage and frequency as of the power grid.
It should have minimal distortion from pure sine wave.
VFD is used as electric drives for motors. Has the capability of changing the frequency for more control over the machine.

## Slide 3: Voltage source vs Current source inverters
VSI
Constant output voltage
Large capacitor placed in parallel to the voltage source
Does not have built in protection against short circuits
CSI
Constant output current
Large inductor placed in series with the voltage source
Has built in protection against short circuits
Notes: Due to the large value of the inductor placed in series with the DC source in CSI. When a short circuit situation arises, the current takes time to rise.
In fact when a H – bridge is used, you should never interrupt the path of current, so it is preferred to short the source before moving on to the next combination of switches.
This would not turn out so good in VSI, where dead zones are specifically added in order to not short circuit the voltage source.
Since I am designing this inverter for electrical machine application its important to also note that:
VSI = Speed Control
CSI = Torque Control

## Slide 4: Pure Sine vs Modified Sine wave inverters
Pure Sine
Smooth Sinusoidal Waveform
Very Low THD (<5%)
Lower Efficiency due to complex control, filtering and high switching frequency
Can be used for sensitive loads too
Modified Sine Inverters
Square-like stepped waveform
High THD (20% - 40%)
Higher efficiency with reduced performance with complex loads
Mainly used for simple loads (Resistive)
Notes: Due to the large value of the inductor placed in series with the DC source in CSI. When a short circuit situation arises, the current takes time to rise.
In fact when a H – bridge is used, you should never interrupt the path of current, so it is preferred to short the source before moving on to the next combination of switches.
This would not turn out so good in VSI, where dead zones are specifically added in order to not short circuit the voltage source.
Since I am designing this inverter for electrical machine application its important to also note that:
VSI = Speed Control
CSI = Torque Control

## Slide 5: Effect of harmonics on motor
Harmonic content makes it harder to magnetize the core. It increases eddy current losses and hysteresis losses.
These losses manifest as additional heat. Heat is always bad for a motor.
Positive sequence harmonics such as the 7th, 13th, 19th increase the torque production.
Negative sequence harmonics such as the 5th, 11th, 17th decrease the torque and act as a brake.

## Slide 6: Why switching, why not amplification?

## Slide 7: Types of Switches

## Slide 8: Gate Driver Types

## Slide 9: Inverter topologies
Simple H – bridge inverter
Multi-level inverter
  Cascaded H – bridge inverter
  Transformer based multi-level inverter
  Diode clamped multi-level inverter
  Flying Capacitor multi-level inverter
Notes: Talk about switches here: Mainly there are three switches 1. BJT
2. MOSFET
3. IGBT
BJT requires current in its base to turn on, less switching frequency.
MOSFET requires voltage at its gate to turn on, high switching frequency, has moderate voltage blocking capability, suitable for high voltage and moderate current
IGBT requires voltage at its gate to turn on, high switching frequency, has high voltage blocking capability, suitable for high voltage and current. So this can be chosen to make electric drives.

## Slide 10: Simple H – bridge inverter
Switching scheme:
S1 | S2 | + VDC
S2 | S3 | 0
S3 | S4 | -VDC
S4 | S1 | 0
Notes: Here L1 & L2 are the terminals of the load
Since this is a Voltage source inverter, it is important to note that (S1 S3) and (S2 S4) are forbidden combinations.
Mention the reason why you’re switching instead of amplifying.

## Slide 11: Cascaded H – Bridge inverter
Requires isolated DC voltage sources.
At the expense of more switches, they allow for multiple voltage levels at the output.

## Slide 12: Flying Capacitor Multi – Level inverter
The figure shows one leg of a multilevel flying capacitor inverter.
The flying capacitor is maintained at 0.5 VDC voltage.
S1 | S2 | +VDC | -
S2 | S3 | 0 | -
S2 | S4 | +0.5 VDC | Discharge
S1 | S3 | +0.5 VDC | Charge
Notes: To get 0.5 Vdc on this leg of the inverter, there are 2 choices. One option would discharge the capacitor and the other option would charge the capacitor. Switching must be such that the capacitor is maintained at 0.5 VDC.

## Slide 13: Why are diodes required?
Inductors cause voltage spikes, these spikes if not mitigated are enough to damage the transistor.
Hence a diode is used to clamp the voltage across the switch.
MOSFETs have body diodes but usually that is not enough.

## Slide 14: Types of Control
Square Wave
Selective Harmonic Elimination
Sinusoidal – Pulse Width Modulation

## Slide 15: Square Wave Control
Simplest method of control for inverters.
180o Conduction Mode.
Switching Frequency = Fundamental Frequency
t | Voltage | Switches
(0, ) | +Vdc | S1, S2
(,2) | -Vdc | S3, S4
 | Voltage | Switches
 | +Vdc | S1, S2
 | -Vdc | S3, S4
Square Wave
Notes: + vdc = S1 S2
-vdc = S3 S4
Describe the switching sequence to generate this wave
Each switch conducts for 180 degrees hence this method is known as 180 conduction mode.
This has a very low switching frequency, hence the switching losses are minimized at the cost of waveform quality.
The peak value of this w

## Slide 16: FFT – square wave control
Square wave contains only odd harmonics.
V() =
DC Bus Utilization = = 0.900
RMS Voltage = Vdc
THD = = 48.3%
Frequency Domain Representation of a Square Wave
Notes: By substituting n = 1, we find that the DC bus utilization is 127%.
Fundamental harmonic magnitude = 1.273Vdc

## Slide 17: Quasi - Square Wave Control
Eliminates all multiples of the 3rd harmonic.
120o Conduction Mode.
Quasi - Square Wave
t | Voltage | Switches
(0, ) | 0 | S4, S1
(,) | +Vdc | S1, S2
(,) | 0 | S2, S3
(,) | -Vdc | S3, S4
(,2) | 0 | S4, S1
 | Voltage | Switches
 | 0 | S4, S1
 | +Vdc | S1, S2
 | 0 | S2, S3
 | -Vdc | S3, S4
 | 0 | S4, S1
Notes: + vdc = S1 S2
-vdc = S3 S4
Describe the switching sequence to generate this wave
Each switch conducts for 180 degrees hence this method is known as 180 conduction mode.
This has a very low switching frequency, hence the switching losses are minimized at the cost of waveform quality.
The peak value of this w

## Slide 18: Quasi - Square Wave Control
Switching Frequency = 2 x Fundamental Frequency
Type of Selective Harmonic Elimination
Quasi - Square Wave
Notes: + vdc = S1 S2
-vdc = S3 S4
Describe the switching sequence to generate this wave
Each switch conducts for 180 degrees hence this method is known as 180 conduction mode.
This has a very low switching frequency, hence the switching losses are minimized at the cost of waveform quality.
The peak value of this w

## Slide 19: FFT – quasi square wave control
V() =
DC Bus Utilization = = 1.103
RMS Voltage = (0.8165)Vdc
THD = = 30.95%
Frequency Domain Representation
Notes: By substituting n = 1, we find that the DC bus utilization is 127%.
Fundamental harmonic magnitude = 1.273Vdc

## Slide 20: SHE – 3rd and 5th Elimination
Eliminates all multiples of the 3rd and 5th harmonics.
Increased switching frequency.
Other harmonics can also be selectively eliminated by adding more segments to this waveform.
Quasi - Square Wave
Notes: + vdc = S1 S2
-vdc = S3 S4
Describe the switching sequence to generate this wave
Each switch conducts for 180 degrees hence this method is known as 180 conduction mode.
This has a very low switching frequency, hence the switching losses are minimized at the cost of waveform quality.
The peak value of this w

## Slide 21: SHE – 3rd and 5th Elimination
Quasi - Square Wave
t | Voltage
(0,) | 0
(,) | +Vdc
(,) | 0
(,) | +Vdc
(,) | 0
(,) | +Vdc
(,) | 0
 | Voltage
 | 0
 | +Vdc
 | 0
 | +Vdc
 | 0
 | +Vdc
 | 0
Notes: + vdc = S1 S2
-vdc = S3 S4
Describe the switching sequence to generate this wave
Each switch conducts for 180 degrees hence this method is known as 180 conduction mode.
This has a very low switching frequency, hence the switching losses are minimized at the cost of waveform quality.
The peak value of this w

## Slide 22: FFT – SHE 3rd and 5th Elimination
DC Bus Utilization = = 0.617
RMS Voltage = (0.534)Vdc
THD = = 63.40%
Frequency Domain Representation
Notes: By substituting n = 1, we find that the DC bus utilization is 127%.
Fundamental harmonic magnitude = 1.273Vdc
By substituting n = 1, we find that the DC bus utilization is 127%.
Fundamental harmonic magnitude = 1.273Vdc ∑_"n=1" ^"∞" ▒〖(−2𝑣_ⅆ𝐶)/𝑛𝜋(cos(𝑛 9𝜋/30) −cos(𝑛 5𝜋/30)+cos(𝑛 19𝜋/30) −cos(𝑛 11𝜋/30)+cos(𝑛 25𝜋/30) −cos(𝑛 21𝜋/30))×sin〗⁡(𝑛𝜔𝑡)

## Slide 23: Selective harmonic elimination - general
The goal in SHE is to prevent certain harmonics from appearing in the waveform at all.
Achieved by precisely choosing the switching angles, so that specific harmonics are mathematically zeroes out in the Fourier Series.
The waveform is shaped to directly avoid producing those frequencies.
Example: 3rd Harmonic elimination, 3rd and 5th Harmonic elimination.
Notes: Based on the number of harmonics, the waveform shape is decided. Based on the specific harmonics to eliminate the switching angles are decided.

## Slide 24: Harmonic cancellation - general
Two similar waveforms, phase shifted in time are added to cancel out specific harmonics.
Happens to 3 phase systems naturally. The line voltages do not have multiples of three harmonics.
Needs extra hardware.
Notes: This waveform is made by shifting the 120 conduction mode by 36 degrees.
3rd and 5th are eliminated. (multiples also).
When you make 3 phase inverters, you need not worry about limiting 3rd multiple harmonics, because they get cancelled out automatically in a balanced system.

## Slide 25: Harmonic cancellation - general
Vx1 =
Vx2 =
Notes: This technique is used very widely in computers. Buck converters don’t output a smooth voltage, they have a ripple. So using a multi phase buck converter you can double the frequency of the ripple and halve the magnitude of it. This makes it 4 times easier for the capacitor to filter it out. Multi phase buck converters.

## Slide 26: Sinusoidal - pwm
Outputs a high frequency square wave with varying pulse widths.
Pulses obtained for:
  First Leg: Compare message signal with the carrier signal.
  Second Leg: Compare inverse of message signal with the carrier signal.
Requires high switching frequencies.
Easy to filter out the high frequency harmonics.
Carrier signal and Message signal for SPWM
Notes: SPWM is a technique used to approximate a sinusoidal output voltage by switching the inverter on and off rapidly in a specific pattern. Instead of generating a true sine wave, the inverter outputs a high-frequency square wave with varying pulse widths, such that the average voltage follows a sine wave.

## Slide 27: Numerical Quantities in SPWM
Vm = Message signal = Sine wave
Vc = Carrier signal = Sawtooth wave
ma = Vm/Vc – Modulation index
mf = fc/fm – Carrier Frequency Ratio
When ma is greater than one, the waveform starts clipping. It is called overmodulation.
Higher mf means more pulses per cycle. It gives better approximation of sine.
Notes: If the sawtooth wave used, is not triangular, then the rising time width and falling time width will no longer be the same. Symmetry in the wave is lost, and even harmonics will also start to appear.
Clipping = Low order harmonics are created.

## Slide 28: How does SPWM work?
A good signal is generated if the integral in a small interval dt, is same for pure sine and pwm.
Notes: If the sawtooth wave used, is not triangular, then the rising time width and falling time width will no longer be the same. Symmetry in the wave is lost, and even harmonics will also start to appear.
Clipping = Low order harmonics are created.

## Slide 29: Implementation – Simple circuit

## Slide 30: Simulation – LTSPICE

## Slide 31: Simulation – LTSPICE

## Slide 32: Simulation – LTSPICE

## Slide 33: Simulation - Simulink

## Slide 34: Simulation - Simulink

## Slide 35: Simulink – Square Wave
Output Voltage Waveform
Current through RL load waveform

## Slide 36: Simulink – Square Wave
Frequency Spectrum of Square Wave

## Slide 37: Simulink – Square Wave
Results:
THD_Voltage = 47.72 %
Load = 1 ohm + 4mH in series
THD_Current = 12.76 %

## Slide 38: Simulink – SHE – 3rd Elimination
Output Voltage Waveform
Current through RL load waveform

## Slide 39: Simulink – SHE – 3rd Elimination
Frequency Spectrum of Square Wave

## Slide 40: Simulink – SHE – 3rd Elimination
Results:
THD_Voltage = 31.01 %
Load = 1 ohm + 4mH in series
THD_Current = 4.99 %

## Slide 41: Simulink – SHE – 3rd & 5th Elimination
Output Voltage Waveform
Current through RL load waveform

## Slide 42: Simulink – SHE – 3rd & 5th Elimination
Frequency Spectrum of Square Wave

## Slide 43: Simulink – SHE – 3rd & 5th Elimination
Results:
THD_Voltage = 63.14 %
Load = 1 ohm + 4mH in series
THD_Current = 7.242 %
Observation – THD of current is greater here than 120 conduction mode.

## Slide 44: Simulink – SPWM
Output Voltage Waveform
Current through RL load waveform

## Slide 45: Simulink – SPWM
Frequency Spectrum of Square Wave

## Slide 46: Simulink – SPWM
Results:
THD_Voltage = 55.26 %
Load = 1 ohm + 4mH in series
THD_Current = 0.5434 %
Carrier Frequency = 5 kHz

## Slide 47: Future work on this project
Implement Bipolar PWM and analyse harmonic content and efficiency.
Extend the design to three phase inverter.
Explore SVPWM technique.
Drive an actual motor with the inverter.
Integrate current control features and enable regenerative braking.